## Slide 1: Handheld scanner
Netum Barcode Scanner

## Slide 2
Netum
Front & Bottom
On/Off

## Slide 3: Unpacking your Handheld
Unpack
Unpack handheld make sure to keep your instruction book
Charge
Charge handheld
USB Dongle
Put the dongle in your computer
Bluetooth
Connect to your Bluetooth via your computer
Dongle
Charge Cord

## Slide 4: Firmware
First Scan firmware bar-code – Scan here before you start anything you will only have to scan the firmware once to setup your devise

## Slide 5
Transmission Speed Via Bluetooth Connection
America EN Keyboard: English lettering
Medium Speed: Scan here for upload speed
Keyboard Language

## Slide 6: Wireless & Bluetooth
Working Vis USB Dongle (Wireless Mode) - Scan bar-code
Bluetooth – Scan working Via Bluetooth bar-code
Bluetooth: Connect to your computer via Bluetooth
Go into your settings then Bluetooth connect click search for devise
USB Dongle: Wireless mode using the dongle to connect to your computer
Put the USB Dongle into a USB port in your computer

## Slide 7
Normal Mode: Scan here if you are Scanning straight to your computer
Store Mode: Scan here to store scans in the handheld devise
Normal Mode: If you are wanting to Scan straight to computer
Store Mode: This mode is to keep the scanned bar-codes in the “memory” of the handheld

## Slide 8: Uploading to Computer
Login into WellSky Service Scan Desktop – Test: Find your job. click on (Highlight) the job you want to upload your scanned units to.
Now scan the output store data bar-code on the next slide (this will upload all the scanned units that are in the scanner)

## Slide 9
Output Stored Data:
Output Total Entry:
Will upload scanned items in job/computer

## Slide 10
Clear Memory: Scan here after you are done with each job to clear out the previously scanned items